## Slide 1: Roaming Revenue Assurance

## Slide 2: Contents
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 3: Introduction to Roaming
7.
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 4: Introduction to Roaming
Definition: Roaming is defined as the ability for a cellular customer to automatically make & receive voice calls, send & receive data, or access other services when travelling outside the geographical coverage area of the home network, by means of using a visited network to do the following
  automatically make and receive voice calls,
  send and receive data,
  or access other services, including home data services
In wireless telecommunications, roaming is a general term referring to the extension of connectivity service in a location that is different from the home location where the service was registered.
Roaming ensures that the wireless device is kept connected to the network, without losing the connection outside the home network
Why Roaming ? The commercial reasons for roaming is that it generates revenue in two different ways:
  When a Operator A customer enters a Operator B market and uses the visited network, the visited network records the call information, rates the call, and bills Operator A.
  Operator A, in turn, re-rates the bill from the visited carrier and bills its subscriber.
Apart from the revenue advantage, it was a basic demand from subscribers, which has eventually proven to be one of the key success factors in the service offering of mobile telephony (e.g. success of GSM technology compared to other technologies has been attributed to roaming capabilities).

## Slide 5: Call flow – Roaming Outgoing Call to other operator in roaming circle
Switch
(MSC)
Called Number
( B Number)
Home Location
(Circle 1)
Visitor Location
(Circle 2)
HLR
Switch
(MSC)
VLR
Calling Number
( A Number)
Switch
(MSC)
Called Location
(Circle 2)
HLR
1
3
4
2
(Authentication)
Call Flow
#1 – Subscriber in roaming circle latched to visited operator and initiates a O/G call
#2 – Visited operator VLR authenticates with the home operator for allow/disallow the call
#3 – Once the authentication is being provided visited operator MSC allows the call
#4 – Call being handed over to other operator and then to the called subscriber

## Slide 6: Call flow – Roaming Outgoing Call to same operator in roaming circle
Switch
(MSC)
Called Number
( B Number)
Home Location
(Circle 1)
Visitor Location
(Circle 2)
HLR
Switch
(MSC)
VLR
Calling Number
( A Number)
1
3
2
(Auth)
Call Flow
#1 – Subscriber in roaming circle latched to visited operator and initiates a O/G call
#2 – Visited operator VLR authenticates with the home operator for allow/disallow the call
#3 – Once the authentication is being provided visited operator MSC allows the call and connect to the called no

## Slide 7: Roaming Incoming Call from other operator in roaming circle
Switch
(MSC)
Calling Number
( A Number)
Home Location
(Circle 1)
Visitor Location
(Circle 2)
HLR
Switch
(MSC)
VLR
Called Number
( B Number)
Switch
(MSC)
Calling Location
(Circle 3)
HLR
4
3
1
2
Call Flow
#1 – Calling number makes a call to the Subscriber whose is in roaming circle latched to visited operator
#2 – Circle 3 Switch will send the call to the roaming subscriber’s home network
#3 – Home network will than check the customer location in its VLR and than forwards the call to the roaming partner
#4 – Roaming partner terminates the call the roaming subscriber

## Slide 8: Roaming Incoming Call from same operator in roaming circle
Switch
(MSC)
Calling Number
( A Number)
Home Location
(Circle 1)
Visitor Location
(Circle 2)
HLR
Switch
(MSC)
VLR
Called Number
( B Number)
4
3
2
1
Call Flow
#1 – Calling number makes a call to the Subscriber whose is in roaming circle latched to visited operator
#2 – Circle 2 Switch will send the call to the roaming subscriber’s home network
#3 – Home network will than check the customer location in its VLR and than forwards the call to the roaming partner
#4 – Roaming partner terminates the call the roaming subscriber

## Slide 9
TAP exchange process
Home Operator
Roaming Partner
Roaming Customer
Latches on to Roaming partner network
All calls made by roaming customer are transited by Roaming partner MSC
All CDR’s generated at RP MSC are being sent to his roaming billing system thru which TAPIN file is being generated and sent to DCH
Data Clearing House
DCH performs the basic validation on the TAP file received from the roaming partner like
File Format
CDR format
Tariff charged
Ageing of CDR
TAPIN received by the home operator and processed in there roaming billing system.
In case of postpaid CDR’s are being sent to postpaid billing for rating
Prepaid CDR’s are being filtered as charging for the same happens online at IN

## Slide 10: General Roaming Terminologies
7.
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 11: General Roaming Terminologies
TAP -The Transferred Account Procedure is the mechanism by which operators exchange roaming billing information. This is how roaming partners are able to bill each other for the use of networks and services through a standard process.
TAPIN -File received from third party operator for customers roaming (using) their network
TAPOUT - File prepared with all visitors on the network. This file is sent to the clearing house or directly to the involved third party operator (operator of which the visitor is a customer)
DCH –Data Clearing House services may be employed by an operator to act as its agent. Data Clearing Houses can provide a single point of contact to send and distribute files to and from roaming partners. Data Clearing Houses (DCH), where employed, are responsible to their customer for the error free transfer of TAP files between the roaming partners.
Roaming in - A wireless-subscriber of a third party operator roaming on your network
Roaming out - A wireless-subscriber of own network roaming on a third party network
SDR(Special Drawing Rights) – Currency used for charging of a calls made by customers in roaming network which is sent in Tap File. an IMF basket currency. For the conversion of SDR into the currency of payment operators must apply the pegged SDR rate quoted by the International Monetary Fund (IMF) on the twenty third (23rd) of the month preceding the invoicing period, or in case this is a US public holiday, the previous business day of the month preceding the invoicing period which is published from IMF.

## Slide 12: General Roaming Terminologies…contd
VPLMN -Visiting Public (Land) Mobile Network -acronym used to indicate a roaming partner on which one of your subscribers is roaming.
HPLMN -Home Public (Land) Mobile Network -network operator of the subscriber that is roaming
CAMEL - Customized Applications for Mobile networks Enhanced Logic is an adaptation of the Intelligent Network (IN) for GSM networks that allows prepaid subscribers to roam seamlessly in other networks an able to charge the prepaid roaming calls on real-time basis.
HUR - High Usage Reports are generated by roaming partners to capture any high usage of roamers on their respective networks. These HURs are provided to roaming partners on a periodic basis as an alert for fraud.
MCC-MCN – Mobile Country Code & Mobile Network Code are used in combination to uniquely identify a mobile phone operator. MCC & MNC are primarily first five digits of the IMSI and are configured in all network elements like Switch & SGSN and IT systems like mediation & Billing System for allowing roaming, rating & billing
Roaming Revenue – Operator will get the roaming revenue when customer from visited operator latches on to his network and does the usage
Roaming Expense - Operator expense will be if his customer latches on to visited network and does the usage there
RCF (Roaming Call Forward) – Forwarding CDR generated at home network to roaming operator when an out roamer of home network receives incoming call.

## Slide 13: Key Concepts
7.
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 14: Key Concepts - TAP
TAP files contain rated call information according to the operator's Inter Operator Tariff (IOT), plus any bilaterally agreed arrangements or discounting schemes.
The TAP files are generated and sent, at the latest, 36 hours from call end time. This means that operators can send 1 or many TAP files per day. Most operators send one TAP file per operator each day.
Additionally, the roaming partners will also agree on High Usage thresholds. These thresholds need to be monitored by the visited operator and High Usage Reports (HUR) need to be sent to the home operator within 36h of the occurrence of the high usage.
TAP files are rated in SDR (Special Drawing Rights), an IMF basket currency. For the conversion of SDR into the currency of payment operators must apply the pegged SDR rate quoted by the International Monetary Fund (IMF) on the twenty third (23rd) of the month preceding the invoicing period, or in case this is a US public holiday, the previous business day of the month preceding the invoicing period which is published from IMF.
The transfer of TAP records between the visited and the home mobile networks may be performed directly, or more commonly, via a Clearinghouse. Invoicing between the operators then normally happens once per month.

## Slide 15: Key Concepts – Data Clearing & Financial Clearing
Data Clearing
    In order to recover roaming revenue, operators need to exchange billing information between each other. It is possible to do this on a peer-to-peer basis, however most operators choose to use Data Clearing Houses to exchange the billing information.
    Data Clearing House services may be employed by an operator to act as its agent.
    Data Clearing Houses can provide a single point of contact to send and distribute files to and from roaming partners.
    Data Clearing Houses (DCH), where employed, are responsible to their customer for the error free transfer of TAP files between the roaming partners.
    In addition to data clearing other services are offered:
        File validation
        File creation
        File conversion
        Fraud detection
        Tariff check
        Invoicing & Payment
Financial Clearing
    In order to recover roaming revenue operators need to invoice each other for the traffic used in the respective networks. It is possible to do this on a peer-to-peer basis, however most operators choose to use Financial Clearing Houses to produce, exchange and clear invoices
    Based on the billing information they receive from the operator (or Data Clearing House where employed), the Financial Clearing House performs some or all of the following functions:
      Produce and distribute invoices on behalf of the operator;
      Provide collection and payment of funds and monitor credit issues
      Reclaim of Foreign VAT
      Provide bilateral or multilateral settlements

## Slide 16: Roaming Revenue Cycle
7.
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 17: Roaming Revenue Cycle
Revenue Cycle for roaming can be broadly broken into 4 parts -
Commercial Agreement
Partner Provisioning
Subscriber Provisioning
Rating & Billing
Signing of document like AA12,13, & 14
IREG & TADIG Testing
Configuration at HLR ,VLR & IN
TAP exchange, rating subscriber billing & prepaid charging

## Slide 18: Roaming Revenue Cycle – Commercial Agreement
Commercial Agreement
Partner Provisioning
Subscriber Provisioning
Rating & Billing
Signing of document like AA12,13, & 14
IREG & TADIG Testing
Configuration at HLR ,VLR & IN
TAP exchange, rating subscriber billing & prepaid charging
AA.12 - International Roaming Agreement
  The basic legal framework set out in AA.12 covers areas such as scope, confidentiality provisions, data privacy, liability, fraud prevention, duration, suspension of services and termination.
AA.13 - Common Annexes
  It agrees the services offered shall be implemented in accordance with relevant specifications.
  Details of TAP, e.g. file transfer schedules and fallback procedure
  Details of the settlement procedure i.e. how/when invoices are to be sent/paid.
  Customer care principles, Technical aspects including usage of test SIMs, security and connections.
  An annex of AA.13 covers fraud prevention procedures, stating time frames for sending and the contents of High Usage Reports.
AA. 14 – Individual Annexes
  Operator Confidential - Information such as the operators IOT, and various contact details for standard business process such as TAP file transfer, invoices exchange and Customer Care telephone and fax numbers.
  Public Domain - The information is more generic, and includes the list of services offered: specific networks settings, coverage areas (that could also include names of towns and villages) and other miscellaneous network information.
In order to enable roaming facility, operators need to enter into Commercial Roaming Agreements.
Roaming agreements with operators in the same country is a relatively simpler process than International Roaming agreement process with operators globally.
Following are the documents which are signed between the operators

## Slide 19: Roaming Revenue Cycle – Partner Provisioning
Commercial Agreement
Partner Provisioning
Subscriber Provisioning
Rating & Billing
Signing of document like AA12,13, & 14
IREG & TADIG Testing
Configuration at HLR ,VLR & IN
TAP exchange, rating subscriber billing & prepaid charging
Establishing the signaling links between the operator and the Roaming partner for roaming services to commence between them.
Exchanging Test SIMs – Test SIMs are exchanged between the roaming partners for initial and ongoing tests to be performed between the two networks. There are two types of GSM tests that need to be performed:
IREG (Inter-Working, Roaming Expert Group) - This function is performing the actual Roaming tests, and trouble shooting for network problems. They will be responsible for ordering the signaling links and opening the network to testing, and later to commercial Roaming
  Testers from both operators place exchanged test SIM cards in a phone and make calls
  The Individual test is a check point for some main services that includes different test cases such as
    Call from a mobile to mobile phone, Call from a mobile to a fixed line, SMS, Call forwarding etc
TADIG (Transferred Account Data Interchange Group) - This function will (on the basis of the data produced when performing the technical roaming testing) perform billing tests. They will be responsible for TAP formats, liaison with Data Clearing House (if used) and managing the TAP file flows between networks on a daily basis
  During the IREG test traffic has been generated in both networks. This traffic is itemized in terms of CDRs (Call Detail Records) and stored in CDR files.
  Each operator has to make sure that the CDRs are included in a test file and sent to the other operator.
  IOT information is needed at this stage to check that the calls are being charged correctly). After an operator has checked the file and the content validated a TCC (TAP Testing Completion Certificate) is issued.

## Slide 20: Roaming Revenue Cycle – Subscriber Provisioning
Commercial Agreement
Partner Provisioning
Subscriber Provisioning
Rating & Billing
Signing of document like AA12,13, & 14
IREG & TADIG Testing
Configuration at HLR ,VLR & IN
TAP exchange, rating subscriber billing & prepaid charging
Each mobile network has its own HLRs and VLRs. When a MSC detects a mobile user's presence in the area covered by its network, it first checks a database to determine if the user is in his/her home area or is roaming, i.e., the user is a visitor.
  User in Home Area: HLR has the necessary information for initiating, terminating, or receiving a call.
  User is Roaming: VLR contacts the user's HLR to get the necessary information to set up a temporary user profile.
The user's location is recorded in the HLR, and in case the user is roaming, it is also recorded in the VLR. Suppose that the user wants to make a call:
  User in Home Area: MSC contacts the HLR prior to setting up the call.
  User is Roaming: MSC contacts the VLR prior to setting up the call.
Suppose that there is a call for the user (call goes to the home MSC):
  User in Home Area: Home MSC delivers the call immediately.
  User is Roaming: Home MSC contacts the VLR to determine the appropriate switch in the roaming area to handle the arriving call and then transfers the call to the roaming area MSC.
Subscriber provisioning involves activation of roaming services against the subscriber’s profile on the HLR based on a formal request from the subscriber. This enables the subscriber to make and receive voice calls, send and receive data and access other services while traveling outside the coverage area of their home network
Generally, postpaid subscribers are set to a profile that does not include roaming by default and operator may charge one time deposit and monthly rental
Prepaid subscribers have access to roaming as a default service if CAMEL technology (explained in detail later in the module) has been implemented on the operator’s network.

## Slide 21: Roaming Revenue Cycle – Rating & Billing
Commercial Agreement
Partner Provisioning
Subscriber Provisioning
Rating & Billing
Signing of document like AA12,13, & 14
IREG & TADIG Testing
Configuration at HLR ,VLR & IN
TAP exchange, rating subscriber billing & prepaid charging
Call made by customer in visited network and CDRs get generated at visitor network MSC and are being sent to the home operator through TAP (Transfer Account Procedure) files either directly or thru clearing house
The clearing house receives TAP files from visiting network operator, performs various pre-determined checks on TAP files (like duplicates, file format, validation of SDR rate, conversion to local currency, etc). and forwards them to the home operator for processing and subscriber billing.
Home operator validates the incoming TAP file and rejects the CDR’s in TAP file if the same are not in correct format or to the terms of the agreement, RAP(Return Account Procedure) files are also generated by Clearing House in case Operators use services of a Clearing House.
Postpaid Subscriber charging for roaming usage is performed in the same way as charging for normal call and data services. As soon as TAP files are received, they are uploaded into the retail billing systems and roaming charges are billed to the subscribers and prepaid roaming CDR’s being filtered from the billing system as the charging has happened online thru CAMEL interface
Based on the TAP files, Roaming settlements between operators are performed in the same way as the Interconnect settlements.
Prepaid Subscriber charging in roaming is online same as calls made in home network thru CAMEL interface, by the home operator itself. However need to verify and deplete subscriber account balances on a real time basis makes prepaid roaming complex
The capability for tracking roaming usage and depleting balance on a real time is permitted by CAMEL. CAMEL roaming is the most commonly used technique to enable prepaid roaming by operators

## Slide 22: Key Risk in Roaming
Sr No | Risk Description | RA Control Activity
1 | Rejection in TAPIN rating & TAPOUT generation. Customer not able to make Outgoing calls in roaming area | MCC-MNC Reconciliation
Configuration Validation
Sr No | Risk Description | RA Control Activity
1 | CDR’s sent by roaming partner but not billed to postpaid/prepaid customer & leading to revenue loss and excess payout | TAPIN CDR vs IN & Billing CDR’s
2 | CDR’s generated at MSC for In roamers but not sent in TAPOUT leading to revenue loss | MSC CDR vs TAPOUT
CDR Reconciliation
Sr No | Risk Description | RA Control Activity
1 | Missing TAPIN files received from roaming partner , non generation of TAPOUT File leading to revenue loss | TAP (IN/OUT) sequence check
Traffic Monitoring

## Slide 23: Key Risk in Roaming…..contd
Sr No | Risk Description | RA Control Activity
1 | Correct Rates are not applied by the roaming partner in the TAPIN sent leading to wrong charging to the customer and excess payout to the roaming partner | SDR Rate Verification for TAPIN files with roaming agreement
2 | Correct Rates are not applied while generating the TAPOUT leading to wrong charging and under billing to the roaming partner | SDR Rate Verification for TAPOUT files with roaming agreement
3 | Prepaid roaming Incoming CDR’s not charged at IN leading to revenue loss and excess payout to the roaming partner | Tapin CDRs vis a vis RCF (Prepaid)
Billing & Rating
Sr No | Risk Description | RA Control Activity
1 | Incorrect configuration & non performance of comprehensive UAT would mean incorrect rating and other issues | New Roaming Partner TAP Validation (IN & OUT)
New Roaming Partner Launch

## Slide 24: Intra Circle Roaming
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 25: Intra Circle Roaming
What is Intra Circle Roaming?
Roaming within circle which enable operators enter into roaming pacts with other operators in the same circle to offer subscribers seamless connectivity in areas yet to be covered by its own network, while it cobbles together the necessary infrastructure
    Benefit subscribers of regional players who are now expanding on a pan-India basis, but are unable to roll out networks covering the entire circle fast enough
    For existing operators, it would open up a new revenue channel
ICR could be one way and both way. One way ICR means that only one operator will roam into the other’s network. In both way ICR, both the operator will use each other network.
In today’s scenario where network layout costs are rising exponentially (owing to increased spectrum and license rates), more and more operators are going in for the ICR approach to provide services in areas where their own network is absent. This reduces the headache of laying one’s own network and leads to a drastic reduction in CAPEX.
Each Sim to have default HPLMN
Preferred roaming partner to be defined by home operator
SIM latched to other operator looks for HPLMN every 20mt
Roaming Network Changes
Roaming operator to convert CDRs in TAP 3.11 format and handover to DCH operator for processing (Operators can also exchange CDR directly between themselves without using DCH)
Both operators to support NRTRDE (Near Real Time Roaming Data Exchange) to avoid frauds
Data Clearing House
All calls to customer care to be routed back to home operator Roaming operator to convert short codes into long and handover
Customer Care

## Slide 26: Intra Circle Roaming….implementation approach
HLR
MSC
SMSC
IN
IN
HLR
MSC
SMSC
Operator 1 STP
Operator 2 STP
Operator 2
Operator 1
All nodes to be connected via Signal Transfer Point (STP)
Address of each node of operator 1 to be stored in Operator 2 STP and vice versa
Every time a node is added in any network, the STP on both sides needs to be updated
Same Circle

## Slide 27: Key Challenges of ICR
Customer Perspective
  Difficulty in logo display in non-self coverage areas
  Potential problems with Operator-specific services in non-self coverage areas
Revenue Perspective
  Loss of revenue from national / international roaming traffic
  Potential loss of NLD/ILD traffic unless the calls are routed back to HPLMN
  Reliance on serving operator for billing information, fraud management and lawful interception
Coordination
  Continuous dialogue with partner so that locations Ids for network expansion is updated on a real time basis.
Marketing
  Higher incentive to retailers / distributors where operator network is not present
Billing
  Processing of TAP files every 6-8 hours
  Re-rating of TAPs as per the customer plan
  Higher payout to DCH
Regulatory
  The Rollout obligation is not reduced by entering into any such agreement.
  Possibility of network congestion in circles where operator 1 is the incumbent operator

## Slide 28: Glossary
8.
Key Concepts
General Roaming
Terminologies
Intra Circle Roaming
Roaming Revenue Cycle
Glossary
1.
Introduction to Roaming
3.
5.
2.
4.
6.

## Slide 29: Glossary
Acronym | Description
CAMEL | Customized Applications for Mobile networks Enhanced Logic
CDR | Call Data Records
IREG | International Roaming Expert Group
MSC | Mobile Switching Centre
PNO | Partner Network Operator
RAP | Reject Account Procedure
SDR | Standard Drawing Rights
TADIG | Transfer Account Data Interchange Group
TAP | Transfer Account Procedure

## Slide 30: Thank you